## Slide 1
BATCH 11
Smart Hostel
Energy Saver System
Automatic room power cutoff using PIR (Passive Infrared) heat detection
when no occupant is present — saving energy, reducing hostel bills.
ESP32 · HC-SR501 PIR · Relay Module · Arduino IDE

## Slide 2
THE PROBLEM
28-30%
of hostel electricity
wasted in empty rooms
₹800+
extra per student per year
due to forgotten lights/fans
~0
existing hostels with
auto power-off systems
Students routinely leave lights and fans running when they step out — lectures, canteen, sports. In a 200-room hostel, this adds up to significant electricity waste every single day.

## Slide 3
OUR SOLUTION
If nobody is in the room,
cut the power. Automatically.
🌡️
PIR Heat Detection
Senses infrared radiation from human body heat — no contact needed
⚡
Relay Auto Switch
Physically cuts power to lights & fan via relay when room is empty
⏱️
5-Min Timeout
Waits 5 minutes after last motion before switching off — no false cuts
💡
Manual Override
Students can override with a button for uninterrupted study time

## Slide 4
COMPONENTS & CIRCUIT
ESP32 DevKit C V4
Main microcontroller — reads PIR, controls relay, runs logic
HC-SR501 PIR Sensor
Detects body heat (infrared) — GPIO 13, range 7m, 120°
Relay Module
Physically switches AC power to room appliances — GPIO 12
LDR Sensor
Ambient light check — only activates at night via GPIO 34 (ADC)
Push Button
Manual 30-min override for continuous use — GPIO 35
LED Indicator
Visual status — ON when relay is active, 220Ω resistor
🔗 Simulated on Wokwi — wokwi.com/projects/456377440609481729

## Slide 5
HOW IT WORKS
1
PIR Scans Room
Constantly detects infrared heat signatures from human bodies
2
Motion Detected
ESP32 reads HIGH signal → timer resets → relay stays ON
3
Room Empty?
No heat detected for 5 continuous minutes
4
Power Cut
Relay switches OFF → lights and fan turn off automatically
if (motion == HIGH && isDark) { lastMotionTime = millis(); setRelay(true); } // 5-min timeout auto-OFF

## Slide 6
FUTURE IMPROVEMENTS
Phase 1 ·
PIR heat detection
Relay auto switch
5-min timeout
LED indicator
Phase 2
LDR ambient light check
Manual override button
2-channel relay (fan + light)
OLED status display
Phase 3
WiFi dashboard (ESP32)
Energy usage analytics
Warden mobile alerts
Central hostel control

## Slide 7
COST ESTIMATE
Component | Qty | Unit Price | Total
ESP32 DevKit C V4 | 1 | ₹350 | ₹350
HC-SR501 PIR Sensor | 1 | ₹65 | ₹65
5V Relay Module | 1 | ₹55 | ₹55
LDR + 10kΩ Resistor | 1 | ₹15 | ₹15
Push Button | 1 | ₹5 | ₹5
220Ω Resistors | 2 | ₹2 | ₹4
LEDs | 2 | ₹5 | ₹10
Breadboard (830pt) | 1 | ₹70 | ₹70
Jumper Wires | 1 | ₹50 | ₹50
USB Cable | 1 | ₹80 | ₹80
PROTOTYPE TOTAL |  |  | ₹704
Production Unit
(Per Room)
PCB Fabrication ₹250
Project Enclosure ₹80 5V Wall Adapter ₹120
Total per Room: ₹1,150
💰 ROI for 100-room hostel
Deploy cost: ~₹1.15 lakh
Est. monthly savings: ₹8,000+
Break-even in < 15 months

## Slide 8
CONCLUSION
A Practical, Low-Cost Solution
for Hostel Energy Management
🌿
Scientifically grounded — PIR genuinely detects human body heat
💰
Cost-effective — ₹1,150/room with fast ROI at hostel scale
🚀
Expandable — WiFi, analytics, and multi-room control ready
Simulated on Wokwi · Ready for Prototype Build